## Slide 1: Memory efficient w-projection with the Fast Gauss Transform
Keith Bannister
Bolton Fellow
CSIRO Astronomy & Space Science
keith.bannister@csiro.au
With Tim Cornwell (now at SKA)

## Slide 2: Outline
What is w-projection?
Why is important?
Gaussian anti-aliasing functions
W-projection with The Fast Gauss Transform
Results
Conclusions

## Slide 3: Conclusions First
This method (Bannister & Cornwell 2013) is one of a class of algorithms knows as ‘Bannister & Cornwell’ algorithms
Theoretically very interesting
But practically useless
C.f. also Bannister & Cornwell 2011.

## Slide 4: W-projection
Antennas usually aren’t on a flat plane in uv (i.e. they have different w)
As you go away from the phase center (e.g. for wide-field imaging at low frequencies):
  Wavefront curvature becomes important
  i.e. The delay compensation for each baseline changes as a function of position on sky
  i.e. Image looks bad

## Slide 5
Cornwell+ 08
Look! Diffraction/curved
wavefronts

## Slide 6
Look!
Image distortion

## Slide 8: The solution: W-projection
Standard Imaging =
  Grid visibilities with antialisaing (AA) function
  Fourier transform the living daylights out of it
+ that w-projection goodness:
  Build the curved wavefront into the convolution function
  i.e. Convolve the AA function by a complex Gaussian:

## Slide 9
Cornwell+ 08

## Slide 10: Gaussian anti-aliasing functions
The w kernel is a complex Gaussian
If the anti-aliasing function is a complex Gaussian
Then the resulting convolution function is also a complex Gaussian

## Slide 11: You can’t keep a Gauss-i-an down
The convolution of 2 Gaussians
Is also a Gaussian
Which is also the product of
2 Gaussians
i.e. a real envelope + complex
chirp
LaTeX drives me crazy
Incidentally the FT is also Gaussian

## Slide 12: The Fast Gauss Transform (Strain 1991 )
Came out of the flurry of activity from the development of the Fast Multipole Method (Greengard & Strain 1991)
2 step process:
  Take the position, width and height of the Gaussian, and update a set of Taylor coefficients on a grid
  Evaluate the Taylor coefficients at every point on the uv plane
It’s parameterized by 2 numbers:
  L - the size of the box in pixels (can be <1 or > 1 in theory)
  p – The number of Taylor coefficients to store & update

## Slide 13: Terminology

## Slide 14: Error pattern
uvplane
image plane
Error from finite range (i.e. truncation of support)
Error from truncation of Taylor series

## Slide 15: Optimisations
For large Gaussians (big w), don’t update all the Taylor coefficients
Make the box size > 1 uv-cell
Play games with error (cheat)

## Slide 16: Predictions
10x less memory bandwidth
than standard gridding
20x more FLOPS
than standard gridding

## Slide 17: Results – L ~ 1
Worst fractional error in image plane

## Slide 18: Error – L~ 2

## Slide 19: Computation time L~1
10-100x slower than normal gridding 
Dominated by CEXP

## Slide 20: Conclusions & ideas
No need to store or calculate convolution functions: shape built into Taylor series
Can parallelize across Taylor coefficients (i.e. each node only stores/updates certain Taylor coefficients)
Tunable gridding error: reduce gridding error with major cycles – so that first major cycles finish quickly
FGT may still have legs:
  Mapping between w and q’ could be better
  Maybe the way I’m using it for complex data is sub-optimal
Can we use the more general fast multipole method for prolate spheroidal wavefunction * w kernel?