## Slide 1: Calibration with StEFCal: progress, advances and successes
Stef Salvini, Stefan Wijnholds

## Slide 2: The Problem
Given
D the observed visibility matrix , M the model sky visibility matrix, n the number of antennas
Minimise
where the Frobenius norm is
the complex gains matrix G is diagonal with 2x2 blocks (one per antenna)
Where each block is given by

## Slide 3: The Problem
Poor scalability of traditional algorithms
Convergence of StEFCal proven for non-polarized case
  O(n2) operations
Extended here to polarized case
  O(n2) operations
Iteratively minimize (normal equations method for SVD):
where and the two columns of Z and D for the j-th antenna are referred by Zj , Dj namely
The problem has split into n 2x2 systems of equations

## Slide 4: Algorithm
Cost per iteration
  44 n2 real operations
Small memory footprint
  Only 2-4 extra vectors required
Data access
  Unit stride across all items of data.
Parallelism
  Very fine grain (each antenna computed independently)
Synchronization
  1 per iteration
Typical number of iterations
  Varied, <= 100 for adequate convergence
Basic Polarized StEFCal

## Slide 5: Algorithm Validation
Alternative Algorithms Used for Results Comparison | 
Name | Description
BFGS | Alternative method using the BFGS method (developed and written by S.Salvini)
Levenberg-Marquardt | Using the LM routine available from MATLAB (lsqnonlin)
Other validation and skies
Description
Computation and checking of the gradient of the minimised function (its entries should be very small at a minimum)
Simulated skies up to 100,000 sources, up to 1,000 calibration sources calibration sources with various degrees of separation from others (between 1 and 10 factor) corruption of gains: random phases; amplitude of diagonal elements between 0.2 and 2; off-2diagonal elements between 0 and 0.2
Real skies (ongoing) LOFAR (thanks to Tammo and Stefan) Meqtrees (Oleg Smirnov): using StEFcal routinely

## Slide 6: Example
100,000 sources
Random position
Intensity exponentialy distributed between 10-4 and 1
Random source polarization
Geometric instrumental polarization included
256 antennas (512 dipoles)
Baseline up to 250 metres
  For ease of imaging
Simple DFT imaging
All calibrations using Stefcal1c
Histogram of source intensities

## Slide 7: Example
Exact Sky
Observed Sky

## Slide 8: Example
10 %
Model include sources up to x % intensity of brightest
Pictures show difference between exact and calibrated sky
1 %

## Slide 9: Example
0.1 %
Model include sources up to x % intensity of brightest
Pictures show difference between exact and calibrated sky
All sources

## Slide 10: Algorithm Variants
Name | Description
1-basic | The basic algorithm Highly parallel (GPUs)
1-relax | stefcal1a modified to use also G[i-2] and G[i-4] to compute G[i] (relaxation) Highly parallel (GPUs)
1-monitor | Stefcal1b modified to act on convergence issues, monitoring the termination conditions Highly parallel (GPUs)
2-basic | Stefcal1a using the latest value of G rather than from the previous iteration (cfr Gauss-Seidel vs. Jacobi iterations) No averaging step Parallel dependencies within each iteration (no GPUs)
2-relax | Stefcal2a with relaxation No averaging step Parallel dependencies within each iteration (no GPUs)
“Bootstrapping” StEFcal consists of solving a smaller problem to low
accuracy to provide initial values for the iteration.
Very effective!

## Slide 11: Comparing StEFCal Versions

## Slide 12: Performance with Problem Size
Sky model including
  512 dipoles
  10,000 sources
  30 calibration sources
  100 iterations for all sizes
Intel Xeon 2650
  2.0 GHz (2.8 with turbo)
  1 core used
  Double Precision
  Peak ~22 Gflops/sec per core from ZGEMM
“Perfect” scaling
  Normalised to n = 500
  Computational costs O(n2)

## Slide 13: Computational Costs
Problem size | No. iterations | Time (sec) | Gflops/sec | % Peak (ZGEMM)
50 | 136 | 0.005 | 3.10 | 14.1%
100 | 122 | 0.005 | 10.85 | 49.3%
200 | 128 | 0.019 | 11.95 | 54.3%
300 | 84 | 0.027 | 12.19 | 55.4%
400 | 90 | 0.051 | 12.40 | 56.4%
500 | 82 | 0.072 | 12.56 | 57.1%
600 | 100 | 0.125 | 12.67 | 57.6%
800 | 76 | 0.177 | 12.07 | 54.8%
1000 | 96 | 0.370 | 11.43 | 52.0%
1500 | 72 | 0.617 | 11.54 | 52.5%
2000 | 74 | 1.121 | 11.62 | 52.8%
3000 | 84 | 2.849 | 11.68 | 53.1%
4000 | 80 | 4.794 | 11.75 | 53.4%

## Slide 14: SKA-1 LFAA Station Calibration - 1
Description | Value
Number of antennas | 256
No. dipoles per antenna | 2
Total number of dipoles | 512
Number of frequencies | 1024
Precision | Single
Convergence required | 1.00E-05
Half-bandwidth for bootstrapping StEFcal | 50
Total Number of iterations for bootstrapping StEFcal | 31875
Average N. Iteration for bootstrapping per frequency | 31.1
Total Number of iterations for full StEFcal | 19814
Average N. Iteration for full StEFcal per frequency | 19.3
Total no. flops for bootstrap | 6.33E+10
Total no. flops for full-size StEFcal | 2.08E+11
Total number of operations (real flops) | 2.71E+11

## Slide 15: SKA-1 LFAA Station Calibration - 2
No. cores | Time (sec) Total (all freq) | Gflops/sec | % CGEMM n-core | peak (CGEMM)
1 | 16.63 | 17.9 | 41.8% | 42.9
2 | 8.34 | 35.8 | 41.9% | 85.4
3 | 5.57 | 53.5 | 42.2% | 126.9
4 | 4.19 | 71.2 | 41.8% | 170.5
6 | 2.90 | 102.9 | 42.0% | 244.9
8 | 2.35 | 127.0 | 42.2% | 300.9
10 | 1.92 | 155.3 | 41.3% | 375.6
12 | 1.72 | 173.3 | 38.3% | 452.0
14 | 1.63 | 182.9 | 36.5% | 501.4
16 | 1.54 | 194.2 | 41.7% | 466.0

## Slide 16: Scalability

## Slide 17: StEFCal in AARTFAAC (1)
AARTFAAC: 288-antenna all-sky monitor for LOFAR
Bi-scalar calibration: non-polarized StEFCal
Factor 35 speed-up!
    N2 instead of N3
    ~8x more iterations
    Net: 288/8 = 36

## Slide 18: StEFCal in AARTFAAC (2)
Tracking calibration
  Idea: exploit smooth behavior of gains over time
  Method:
    Use gain solution from previous iteration as initial guess
    Do only one (!) full-iteration of StEFCal
  Result: another factor of ~8 reduction
Risk of solution wandering off with time
  Solution: calibration to convergence at regular intervals
Ref: Prasad et al., A&A, in prep. (to be submitted soon)

## Slide 19: Current work
Non-polarized StEFcal
  Extensions
    Minimization of phases only
    Minimization over multiple snapshots
Linear and Polynomial calibration over multiple snapshots (both over time and frequency)
  Experimental code being tested and assessed
  Non-polarized case
  Polarized case
Full-Pol StEFCal
  Testing within pipelines and real data (LOFAR, etc)
    Tammo’s previous talk
  Oleg Smirnov: sliding window, deep imaging with VLA
  Implementation on GPUs

## Slide 20: Any Questions ?
Thank you!
Any Questions?