## Slide 1: Back-end signal processing
CSIRO Astronomy and space science
John Tuthill | Digital Systems Engineer
25 September 2012
Star-on Machine
Dr. Seuss - The Sneetches and Other Stories

## Slide 2: Outline
What is “back-end signal processing”
FX vs XF correlators
Filterbanks
Sampling and ADCs
CABB and ASKAP digital back-ends
Calculation engines
Further reading

## Slide 3: Back-end processing for Synthesis Imaging
Electric field at the remote source propagated to the observing points
down-conversion
X
X
Sampling
Spatial Coherence function or “visibilities”
Back-End
Digital Signal Processing
Correlator
Intensity distribution of the source
Imaging: calibration, 2D FFT, deconvolution
Image:
Shaun Amy

## Slide 4: Spectral Channelisation
Interested in obtaining the cross-correlations (visibilities) across a range of separate frequency channels:
  Spectral line observations – narrow bandwidth
  Continuum – wide, contiguous bandwidth
  Excising channels with high RFI
  Others? Fast transients
Different astrophysics will have different requirements for frequency resolution, total bandwidth and band segmentation.
The back-end signal processing has to be flexible to cater for many conflicting science requirements.

## Slide 5: Correlation
Bring the desired signals up out of the noise
Produce the visibilities for synthesis imaging
Delay
1.134s
+
Noise
Correlator
+
Noise
0 seconds delay
Delay = 1.134 seconds
Note:
Temporal not spatial coherence

## Slide 6: FX and XF Correlators
XF architecture
FX architecture
NxD
D
D
D
FFT
Frequency Channelisation (eg FFT)
Frequency Channelisation (eg FFT)
ATCA before CABB
EVLA (FXF)
ALMA (FXF)
CABB (PFX)
ASKAP (PFX)
DiFX
Convolution theorem

## Slide 7: Filterbanks: FFT vs Polyphase Filters
768-point FFT
12,288-tap polyphase filter + 768-point FFT
One sub-band

## Slide 8: Filterbanks: Polyphase decomposition
Standard single-channel
down converter
H(Z)
Digital
low-pass filter
x(n)
y(n,k)
M-to-1
down-sampler
y(nM,k)
x(n)
y(nM,k)
S
x(n)
r(nM,0)
M-point
FFT
r(nM,M-1)
r(nM,1)
M-path Polyphase
down converter
M-path Polyphase
channeliser
Equivalency Theorem
  Exchange mixer and low-pass filter with a band-pass filter and a mixer.
Re-write the band-pass filter in “M-path form”
Noble Identity
  Move a down-sampler back through a digital filter

## Slide 9: Sampling:
The Sampling Theorem: A band-limited signal having no frequency components
above fmax can be determined uniquely by values sampled at uniform intervals
of Ts satisfying:
fs
2fs
-fs
signal in
anti-alias
filter
ADC
Clean
Aliased
Aliasing
fs
2fs
-fs
Notes: Albinoni Oboe Concerto D minor

## Slide 10: Sampling: ”ideal” Analogue to Digital Converter (ADC)
Quantisation in
time
Quantisation in
amplitude
Discrete-time series of digital numbers out
at N-bits of resolution
signal in
2N-1 discrete levels
between full-scale inputs
SNR for an 8-bit converter = 50 dB
For a full-scale sinusoidal input:
anti-alias
filter
ADC
Notes: Under reasonable assumptions: Uncorrelated with input
Quantisation efficiency

## Slide 11: Sampling: the real-world (especially for high-end ADC’s )
ADC characteristics:
Aperture delay/width
Acquisition time
Aperture jitter
Crosstalk
Missing codes
Differential/Integral nonlinearity
Digital feed-through
Offset and Gain error
Intermodulation distortion
Interleaving errors (high-speed ADC’s)
Spurious-free dynamic range (SFDR)
Dynamic performance relative to
the ideal ADC quantisation noise
Effective Number Of Bits (ENOB)
Ratio of the rms amplitude of the fundamental to the
rms value of the next-largest spurious component (excluding DC)

## Slide 12: Sampling…why go digital at all?
At an instance of time, a digital signal can only represent a value from a finite set of distinct symbols.
By contrast, an analogue signal can represent a value from a continuous (infinite) range.
Surely analogue is more ‘economical’.
So why are digital systems so common place?

## Slide 13: Sampling…why go digital at all?
are, to a degree, immune to noise.
are amenable to regeneration after noise contamination/signal dispersion, without the introduction of errors.
can be coded in order to facilitate error detection.
systems with repeatable and reliable functionality
Digital Systems:
3.3V
5V
1.7V
0V
Logic 1
Logic 0
3.3V
5V
1.7V
0V
3.3V
5V
1.7V
0V
Inverter
Noisy input
Clean output
Much of the effort in the design of the digital back-end hardware/firmware is to ensure these properties hold.
Noisy digital signal

## Slide 14: Compact Array Broadband Backend (CABB)
Analogue-to-Digital converters
Primary filterbanks
up to 2048 channels
4 modes: 1, 4, 16 and 64MHz resolution
Fine Delay and Fringe rotator
f1
f2
Dual-band,
dual polarisation down conversion
2GHz bands
4.096GS/s 9-bits
(6-ENOB)
e-VLBI
Coarse delays
D
Secondary filterbanks
16 overlapping windows 2048 channels/window
(resolution depends on primary filterbank mode)
Pol. A
Pol. B
“F” outputs to
correlator
engines
auto- and cross-polarisation correlations
(calibration)
Continuum
Spectral line
Per antenna

## Slide 15: CABB Correlator
6 x (6-1)/2 = 15 baselines
Full Stokes parameters

## Slide 16: CABB Configurations
CABB Configuration | Primary band | Secondary band (zoom)
CFB 1M-0.5k | 1.0 MHz | 0.488 kHz
CFB 4M-2k* | 4.0 MHz | 1.953 kHz
CFB 16M-8k* | 16.0 MHz | 7.812 kHz
CFB 64M-32k | 64.0 MHz | 31.250 kHz
* Not yet implemented

## Slide 17: ASKAP digital back-end
Analogue-to-Digital converters
First stage filterbank
304 x 1 MHz channels
188 PAF ports
768 MS/s, 8-bits
Per antenna
Data throughput reduced by a factor of 3
Cross-connect
S
NarrowbandBeamformers
Second stage filterbank
Array Covariance Matrix
36 dual-polarised beams on the sky
To correlator engine
16,416 x 18.52kHz channels
2Tbits/s
Off-line beam weight computation
Fine Delay and Fringe rotator
Cross-connect
Hardware Correlator
36 dual-polarised beams from 36 antennas, 16,416 fine channels
To remote imaging supercomputer
D
D
~720 Tbits/s
Notes: Three important differences:
PAF
Mid-stage Beamformer
Fine channels are computed for ALL the input bandwidth (averaged after the correlator for continuum observing)

## Slide 18: Calculation Engines: so many choices…
Hard-wired logic
Stored (programmed) logic
EVLA
ALMA
CABB
ASKAP
MWA
MeerKAT
ASIC’s
FPGA’s
GPU’s
CPU’s/DSP’s
Application-Specific Integrated Circuit
Field Programmable Gate Array
Graphics Processing Unit
Central Processing Unit/ Digital Signal Processor
DiFX
Less flexible
Lower power/computation
Higher initial development
More flexible
Higher power/computation
Lower initial development

## Slide 19
Radio Astronomy:
  H. C. Ko, “Coherence Theory in Radio-Astronomical Measurements,” IEEE Trans. Antennas & Propagation, pp. 10-20, Vol. AP-15, No. 1, Jan. 1967.
  G. B. Taylor, G. L. Carilli and R. A. Perley, Synthesis Imaging in Radio Astronomy II, Astron. Soc. Pac. Conf. Series, vol. 180, 2008.
CABB
  W. E. Wilson, et. al. “The Australia Telescope Compact Array Broadband Backend (CABB): Description & First Results,” Mon. Not. R. Astron. Soc., Feb. 2011
ASKAP
  D. R. DeBoer, et.al, “Australian SKA Pathfinder: A High-Dynamic Range Wide-Field of View Survey Telescope,” Proc. IEEE, 2009.
Filter Banks
  R. E. Crochiere and L. R. Rabiner Multirate Digital Signal Processing, Prentice Hall, 1983.
  f. j. harris, Multirate Signal Processing for Communication Systems, Prentice Hall, 2008.
  P. P. Vaidyanathan, Multirate Systems And Filter Banks, Prentice Hall, 1992.
Beamforming
  B. D. Van Veen and K. M. Buckley, “Beamforming: A Versatile Approach to Spatial Filtering,” IEEE ASSP Magazine, April 1988
Further Reading…

## Slide 20: Thank you
CASS
  Dr John Tuthill Digital Systems Engineer
    t +61 2 9372 4392
    e John.Tuthill@csiro.au
    w www.csiro.au/
CASS - Digital Systems