## Slide 1
CSIRO; Swinburne
Error Recognition Emil Lenc University of Sydney / CAASTRO www.caastro.org
CASS Radio Astronomy School 2012
Based on lectures given previously by Ron Ekers and Steven Tingay

## Slide 2: Error Recognition
Some are hard to fix
Some are easy to fix
Some errors are easy to recognise

## Slide 3: Where do errors occur?
Most errors and defects occur in the (u,v) plane
  Measurement errors (imperfect calibration).
  Approximations made in the (u,v) plane.
  Approximations made in the transform to the image plane.
Some are due to manipulations in the image plane.
  Deconvolution.
What we usually care about are effects in the image plane (not always).
The relative contribution of certain errors will vary depending on the nature of the observation.

## Slide 4: Image or (u,v) plane?
We need to work between the (u,v) plane and the image plane.
  Different types of errors may be more obvious in one plane than the other.
  A good understanding of the relationship between both planes helps (see John Reynold’s talk on Fourier Transforms).
Errors obey Fourier transform relations.
  Narrow features transform to wide features and vice versa.
  Symmetries important – real/imaginary, odd/even, point/line/ring.
  The transform of a serious error may not be serious!
  Some effects are diluted by the number of other samples.

## Slide 5: General form of errors
Additive errors (out-of-field sources, RFI, cross-talk, baseline-based errors, noise)
  V + ε  I + F[ε]
Multiplicative errors (uv-coverage effects, gain errors, atmospheric effects)
  Vε  I ★ F[ε]
Convolutional errors (primary beam effect, convolutional gridding)
  V★ε  IF[ε]
Other errors
  Bandwidth and time average smearing.
  Non-coplanar effects
  Deconvolutional errors
  Software!!!

## Slide 6: Error Diagnosis
If ε is pure real, then the form of the error in the (u,v) plane is a real and even function i.e. F[ε] will be symmetric: ε(u,v) = ε(-u,-v)
  Such errors are often due to amplitude calibration errors.
If ε has an imaginary component, then the form of the error in the (u,v) plane is complex and odd i.e. F[ε] will be asymmetric: ε(u,v) ≠ ε(-u,-v)
  Such errors are often due to phase calibration errors.
Short duration errors
  Localised in uv plane but distributed in image plane.
  Narrow features in (u,v) are extended in orthogonal direction in image.
Long timescale errors
  Ridge in uv plane causes corrugations in image plane
  Ring in uv plane causes concentric “Bessel” rings in image plane

## Slide 7: Gain Errors
Adapted from Myers 2002
10 deg phase error
anti-symmetric ridges
20% amp error
symmetric ridges

## Slide 8: Additive Errors: RFI
Dirty Map
PSF
Observation of 1 Jy source

## Slide 9: Finding RFI
Observation of 1 Jy source
See Mark’s talk for more on removing RFI.

## Slide 10: The Bigger Picture

## Slide 11: The Bigger Picture

## Slide 12: The Bigger Picture
>6 deg!

## Slide 13: The Bigger Picture

## Slide 14: Multiplicative Errors
Dirty Map
PSF

## Slide 15: Primary Beam Error
Deconvolved
Peeled
Peeling applicable to transient and variable sources too.

## Slide 16: Point Deconvolution Errors
Pixel centred
Pixel not centred

## Slide 17: Point Deconvolution Errors

## Slide 18: Point Deconvolution Errors

## Slide 19: Deconvolution Errors (Large-scale Structure)
True sky
Standard CLEAN
Standard CLEAN does not handle large-scale structure well – results in negative bowls. More modern algorithms such as Multi-scale CLEAN are necessary to minimise deconvolution errors (see Urvashi’s talk).

## Slide 20: Wideband Deconvolution Errors
Dirty Image (2.1 GHz CABB Obs)
PSF

## Slide 21: Wideband Deconvolution Errors
Deconvolved Image
Standard CLEAN

## Slide 22: Wideband Deconvolution Errors
Source SED
What standard CLEAN fits with

## Slide 23: Wideband Deconvolution Errors
Deconvolved Image
Multi-frequency CLEAN (see Urvashi’s talk)

## Slide 24: Missing short baselines
No short baselines
Paul Rayner 2001
Can only be fixed with additional data. See Shari’s talk on observing strategies.

## Slide 25: Smearing Errors
Bandwidth average smearing
Average 512x1MHz band
Time-average smearing
Averaging 1000s

## Slide 26: Finding the errors in your way
Avoid sausage factory processing (at least initially)
  Try to understand each processing step.
  Look closely at the data after each step, check and image calibrators.
  Does the data look plausible.
Take a different perspective
  Look at your data in different domains (time, uv, image, frequency).
  Plot different combinations of variables in different spaces.
  Look at residuals, FT your dirty image, FT your beam.
Process your data in different ways
  Try different software, algorithms.
  Partition and process your data in different ways
  Try split in time chunks, split up frequency band
  Different weighting, different uv tapers.

## Slide 27: Error reduction …
Process
Have errors been beaten to submission?
Determine greatest contributing error
Do Science
Attempt to reduce effect of error
No
Yes

## Slide 28: What’s happening?
5.5 GHz observation, 3 configurations, 2 GHz bandwidth
2000:1 dynamic range

## Slide 29: What’s happening
Amplitude calibration errors.
Hot spot near edge of 4.5 GHz beam (outside 6.5 GHz beam)
  Causes steepening of source spectra.
  Causes position dependent effects.
  Will need to consider peeling techniques.
Spectral variation throughout the image (flat and steep)
  Must use multi-frequency deconvolution.
Structures on many different scales.
  Must use appropriate deconvolution algorithms.
North-west hot spot is bright and slightly extended.
  Difficult to deconvolve accurately.
  Small cell size or uv-subtract component.

## Slide 30: What’s happening?
38,000:1 dynamic range