## Slide 1: The Zero/Short Spacing Problem
CSIRO Astronomy and Space Science
2 October 2014
ATCA – Australia Telescope Compact Array
ATNF Synthesis Imaging School 2014
Megan Johnson
Parkes RadioTelescope
+
Notes: ASKAP Picture by Maxim Voronkov (CASS).

## Slide 2
Introduction What is Short Spacing? Correcting for Short Spacing Tools for Interferometer + Single Dish Data Combination

## Slide 3: Introduction What is Short Spacing? Correcting for Short Spacing Tools for Interferometer + Single Dish Data Combination

## Slide 4: Higher resolution allows us to study details of objects like galaxies.
CREDIT: Minchin et al., NRAO/AUI/NSF (HSA);
Travis Rector, Gemini Observatory, AURA (optical).

## Slide 5: Bigger dishes have higher resolution.
θ[rad] ≈ λ / D
D
Notes: Lovely demonstration from NGC 660 data of why higher resolution is cool

## Slide 6: Telescopes with high resolutions are needed to study distant objects.
Local
Group
Local
Volume
HII region
MW
1 kpc
20cm
Parkes
GBT/
Effelsberg
Arecibo
Slide Courtesy of Amanda Kepley, NRAO

## Slide 7: Very large dishes have to be supported against gravity/wind.
14 November 1988

## Slide 8: Very large dishes have to be supported against gravity/wind.
15 November 1988

## Slide 9: You can get higher resolution by splitting up a single dish into smaller dishes…

## Slide 10: and placing them far apart.

## Slide 11
Introduction What is Short Spacing? Correcting for Short Spacing Tools for Interferometer + Single Dish Data Combination

## Slide 12: The signals between the different dishes are correlated together.
d = baseline
d sin θ
θ
Visibilities
Fourier
Transform
Images
Slide Courtesy of Amanda Kepley, NRAO

## Slide 13: Interferometers are analogous to double slits!
λ / D
λ / d
D
λ / D
d = baseline
Slide Courtesy of Amanda Kepley, NRAO

## Slide 14: The resolution goes as the distance between the dishes, not the dish size.
d
Long baselines = high resolution
Short baselines = low resolution
θ[rad] ≈ λ / d
Slide Courtesy of Amanda Kepley, NRAO

## Slide 15: Interferometers are only sensitive to a range of spatial scales because d ≠ 0
Resolution
Largest Angular Scale
Slide Courtesy of Amanda Kepley, NRAO

## Slide 16: Short Spacing Problem
Braun & Walterbos 1985
Ideal
Minus Short
Spacing
Effect of missing
short spacing
Observed Spatial Frequencies
Instrumental Response
Negative
Bowls

## Slide 17: Short Spacing Problem – Interferometer FT View
NGC 1569
  Dirty Cube – single channel shows ugly negative bowls
  FFT of channel shows missing flux in center

## Slide 18: Short Spacing Problem – Interferometer FT View
Looks insignificant, but the center pixel is where ALL of the flux in the image is defined!

## Slide 19: BECAUSE…

## Slide 20: Introduction What is Short Spacing? Correcting for Short Spacing Tools for Interferometer + Single Dish Data Combination

## Slide 21: CLEAN extrapolates inner flux
Amplitude
uv-distance
?
?
?
FFT of “Dirty” Interferometer map
CLEAN model
No information on extended structures!
Shortest Baseline
Observed

## Slide 22: Ekers & Rots Theorem
An interferometer doesn’t just measure angular scales θ≈λ/d it actually measures λ / (d - D) < θ < λ / (d + D)
d
d + D
d - D
D
“Fourier Coverage”
(Slide courtesy of Juergen Ott, NRAO)
d
d + D
d - D

## Slide 23: Ekers & Rots Theorem
Sounds great but you can’t get all that extra information from a single visibility
Interferometers measure a number per baseline and integration time, not a range
Similar to a single dish, you have to scan to get the extra “spacings”
Mosaicing is a way to perform this scanning and unlocks the extra information
(Slide courtesy of Juergen Ott, NRAO)

## Slide 24: Ekers & Rots Theorem
(Slide courtesy of Juergen Ott, NRAO)

## Slide 25: Centaurus A: 406 pointings!
Feain et al. 2011
(Slide courtesy of Juergen Ott, NRAO)

## Slide 26: Interferometer + Single Dish
+
100 meters
43 meters

## Slide 27: Interferometer + Single Dish
+
64 meters
31 meters

## Slide 28: Single Dish – FT View
NGC 1569
  GBT Cube – single channel shows all flux
  FFT of channel shows all flux is in center

## Slide 29: Using a Single Dish (SD) to Correct for Zero Spacing
Get an interferometric observation
Go to a SD and map the same region, use a SD with a diameter larger than the shortest baseline of your interferometric map
Goals:
Aim for (at least) same surface brightness sensitivity at shortest baseline and SD
Calibrate, calibrate, calibrate!
Methods for Combining:
Feathering: FT SD map  FT cleaned, interferometric map  combine both with weighting in uv-space  FT back to combined image
Use the SD map as a model for deconvolution with (multi-scale-)clean
Minimize Maximum Entropy χ2 for both the SD and the interferometric map simultaneously
Linear Combination in image domain
(Slide courtesy of Juergen Ott, NRAO)

## Slide 30: Using a Single Dish (SD) to Correct for Zero Spacing
Get an interferometric observation
Go to a SD and map the same region, use a SD with a diameter larger than the shortest baseline of your interferometric map
Goals:
Aim for (at least) same surface brightness sensitivity at shortest baseline and SD
Calibrate, calibrate, calibrate!
Methods for Combining:
Feathering: FT SD map  FT cleaned, interferometric map  combine both with weighting in uv-space  FT back to combined image
Use the SD map as a model for deconvolution with (multi-scale-)clean
Minimize Maximum Entropy χ2 for both the SD and the interferometric map simultaneously
Linear Combination in image domain
(Slide courtesy of Juergen Ott, NRAO)

## Slide 31
Overlap Region = fluxes should be equal, but single dish is convolved with the beam
= 100 meter dish
= 43
meters for shortest baseline

## Slide 32: Feather – Combine in uv-plane
+
FT EVLA Clean Data Cube
FT GBT Data Cube
=

## Slide 33: Feather – Weights
Amplitude
uv-distance
FFT of “Clean” Interferometer map
FFT of SD map

## Slide 34: Feather – Weights
Amplitude
uv-distance
FFT of “Clean” Interferometer map
FFT of SD map
Interferometric weighting = 1-FFT(SD beam)

## Slide 35: Feather – Weights
Amplitude
uv-distance
FFT of weighted SD + Interferometer map

## Slide 36: Example: Supernova Remnant CTB80
+
Images courtesy of Anish Roshi, NRAO

## Slide 37
Image courtesy of Anish Roshi, NRAO

## Slide 38: Introduction What is Short Spacing? Correcting for Short Spacing Tools for Interferometer + Single Dish Data Combination

## Slide 39: Software Packages for Data Combination using Feathering
AIPS
  task “IMERG”
  have to have input cubes on same pixel and frequency scale
MIRIAD
  task “Immerge” (similar to AIPS task)
CASA
  task “Feather”
  Re-grids input cubes and transforms coordinate system, if necessary
  New!! Lots of potential, still working on applications

## Slide 40: CASA: Common Astronomical Software Applications
(New) software package designed for ALMA (Atacama Large Millimeter/submillimeter Array) data reduction and for EVLA (Extended Very Large Array)

## Slide 41: Feather GUI in CASA (ver 4.1)
New Feather Gui in CASA 4.1.0
  from command line, > casafeather

## Slide 42
Combining ALMA and Mopra mm-data
ALMA (1.7”)
HNCO mosaic of the Brick
Rathborne et al. (2014, in prep). – ALMA 13-point mosaic (5h, 25 antennas); field 3’ × 1.5’.
Mopra (38”)
Images courtesy of Jill Rathborne, ATNF

## Slide 43
Combining ALMA and Mopra mm-data
ALMA (1.7”)
HNCO mosaic of the Brick
Rathborne et al. (2014, in prep). – ALMA 13-point mosaic (5h, 25 antennas); field 3’ × 1.5’.
ALMA+Mopra
Images courtesy of Jill Rathborne, ATNF

## Slide 44
Rathborne et al. (2014, in prep). – ALMA 13-point mosaic (5h, 25 antennas); field 3’ × 1.5’.
Notes: Fade from single dish to ALMA image (3mm continuum)
Beam is in the lower left corner

## Slide 45
HI Single Dish + Interferometer Using MIRIAD task “IMMERGE”
ATCA
ATCA + Parkes
LMC
HI mosaic (1344 pointings) of the Large Magellanic Cloud by Kim et al. (1998, 2003).
Images courtesy of Bärbel Koribalski, ATNF

## Slide 46: Summary
Interferometers are very good at increasing resolution at long wavelengths BUT…
Short-spacing is a problem in interferometry data
  Cannot image extended emission with interferometer if emission is larger than shortest baseline resolution
Methods to combine single-dish and interferometer data
  Feather data together – combine in uv-plane
  use single-dish as model for deconvolution
  Minimize maximum entropy χ2 for both the SD and the interferometric map simultaneously
  combine in image plane with linear combination methods
Software packages available for data combination:
  MIRIAD
  AIPS
  CASA

## Slide 47: Additional References:
Stanimirovic (2002) ASP Conf. Series 278
Sault & Killeen (2003) Miriad Users Manual
Holdaway (1999) ASP Conf. Series 180
Other work (partial list):
    Adler et al. (1992, ApJ, 392, 497); Bajaja & van Albada (1979, A&A, 75, 251); Cornwell, Holdaway & Uson (1993, A&A, 271, 697); Roger et al. (1984, PASA, 5, 560); Schwartz & Wakker (1991, ASP Conf. Ser. 19); Vogel et al. (1984, ApJ, 283, 655); Wilner & Welch (1994, 427, 898); Ye, Turtle & Kennicutt (1991, MNRAS, 249, 722); Kurono et al. (2009, PASJ, 61, 873)
Ekers & Rots (1979) Image Formation, IAU Coll 49, 61.
Cornwell (1988) A&A, 202, 316.
Cornwell (1989) ASPC 6.
Cornwell, Holdaway & Uson (1993) A&A, 271, 697.
Sault, Staveley-Smith & Brouw (1996) A&A Suppl., 120, 375.
Holdaway (1998) ASPC 180, ch.20.
Gueth & Guilloteau (2000) ASPC 217, 291.
Sault & Killeen, miriad manual, ch.21.
Subrahmanyan (2004) MNRAS, 348, 1208.
Bhatnagar, Golap & Cornwell (2005) ASPC 347, 96
Bunn & White (2007) ApJ, 655, 21.
Hull et al. (2010) PASP, 122, 1510.
Pety & Rodriguez-Fernandez (2010), A&A, 517, A12
Bibliography courtesy of Lister Staveley-Smith