## Slide 1: Observing Strategies and the art of Science Proposal Writing Shari Breen | University of Sydney Research Fellow CASS Radio School, Narrabri, September 2017

## Slide 2: Outline
Why is a good observing strategy important?
Things to think about
  What, when, for how long, frequency, array, overheads, CABB mode?
Observing
  The simple cm case
  Slightly less simple cases
  The mm case
  Spectral lines
Turning your plan into a winning proposal

## Slide 3: The importance of a good strategy
  Starts taking shape at the proposal stage
Good telescopes are generally oversubscribed (ATCA usually by 2 – 3 times)
Need to have a good plan to get good data that meets your science goals
Make sure you are familiar with the current status of the instrument

## Slide 4: Lots of resources
Talk to postdocs, other ATCA users, ATNF “friend”, DAs etc and http://www.narrabri.atnf.csiro.au/observing/
The ATCA users guide: http://www.narrabri.atnf.csiro.au/observing/users_guide/html/atug.html
The ATCA forum: https://atcaforum.atnf.csiro.au/
ATCA current issues: https://www.narrabri.atnf.csiro.au/observing/CurrentIssues.html
CABB: https://www.narrabri.atnf.csiro.au/observing/CABB.html
OPAL: http://opal.atnf.csiro.au/

## Slide 5: Things to think about – 1) What?
Strategy dependent on science/object!
  Complicated extended structure?  might need multiple array configs and single dish data
  Point source?  a handful of short cuts over several hours might be enough
  Know where your object is and just need a flux measurement or spectrum?  1 short observation might be enough
  Shadowing?
  Confusion?
  Location? Dec 0?
  Mosaic? (primary beam /D)
  Continuum and/or spectral line?
Cornwell & Feain
Kim et al.

## Slide 6: Things to thing about – 2) When?
Variable source?
  observe when it is expected to be bright
  Or track the flux with observations spread over multiple epochs
Coordination with other telescopes?
Weather?
  Atmosphere generally more stable during winter and at night  better mm observing
  Generally less interference at night at the lower frequencies too (man made and solar)
  Thunderstorms during afternoon in summer
Felli et al. (2007)
Sanna et al. (2009)

## Slide 7: Things to think about – 3) Frequency?
Usually driven by science
  Lines?
  Remember to consider how the telescope performs at different frequencies
  Spread the 2 IFs as far apart as possible, or continuous coverage?
  Take the receiver limitations into consideration (e.g. the 13cm receiver works between 1.1 and 3.1 GHz)
  ‘Standard’ continuum frequencies
16700
21200

## Slide 8: Things to think about – 4) For how long?
Mostly dictated by required sensitivity
  Effective BW and spectral resolution
UV coverage (e.g. bright spectral lines)
  Short integrations across a range of hour angles increases overheads BUT may be the most efficient use of time to cover many sources
http://www.narrabri.atnf.csiro.au/myatca/interactive_senscalc.html

## Slide 9: Things to think about – 5) Array?
Dictated by:
  the resolution required
  uv-coverage requirements (specific arrays work well together – 6A, 6C, 1.5B, 1.5D)
  What’s offered
  Where your source is – shadowing?

## Slide 10
Virtual interferometer
https://crpurcell.github.io/friendlyVRI/

## Slide 11: Things to think about – 6) Calibration and other overheads?
Primary (flux density) calibration
  1934-638 at most frequencies (Uranus/Mars at 3mm)
Bandpass calibration
  1934-638 strong enough at most cm wavelengths
  1253-055 or 1921-293 often used at higher frequencies
Phase calibration (~2min every 40min)
  Unresolved, strongish source within about 10 degrees of target
Pointing calibration
  Carried out every hour at all mm frequencies on a source within ~20 degrees of target
Other overheads
  Set up, slewing,…..

## Slide 12
Cycle time
http://www.narrabri.atnf.csiro.au/calibrators/calcycle.html

## Slide 13
Two x 2 GHz wide IFs (2048 x 1 MHz channels)
  Where you can put them depends on the frequency and your science
Things to think about – 7) CABB mode?

## Slide 14
Optional zoom windows (currently 32 x 1 MHz zooms, or 32 x 64 MHz zooms each with 2048 channels or a hybrid mode)
  Concatenate zoom windows for more velocity coverage
  What mode depends on velocity res/coverage needed
Things to think about – 7) CABB mode?

## Slide 15
Schedule files https://www.narrabri.atnf.csiro.au/observing/sched/cabb/

## Slide 16
Need to calculate sky frequencies
  All done by the CABB scheduler
Schedule files – adding line observations…

## Slide 17
If you are prepared the actual observing is not hard
A simple cm continuum observation of a single source may go something like
  Observe 1934-638
    Do initial array calibration (delays, phases, amplitudes; dcal, pcal, acal)
    Close junk file
    Track 1934-638 for primary and bandpass calibration (~10min)
  Go to target schedule which contains
    Phase calibrator (~2min)
    Target (~20 – 40 min)
    Loop through target schedule until the end (start 1/99 or 1-2/99)
Observing – the simple cm case

## Slide 18
Calibrating the array
dcal
acal
pcal

## Slide 19
Lower frequencies (~2.1 GHz)
  Second IF is redundant
  Lots of interference  need to choose channel range for calibration carefully (set “tvchan”)
  More chance of confusion
Higher frequencies
  1934-638 gets too weak for setup and bandpass  use a stronger source (e.g. 0537-441, 1253-055, 1921-293)
  Observe 1934-638 or a planet at 3mm for primary calibration
  fewer calibrators
The less simple cases

## Slide 20
Everything becomes more difficult at mm frequencies
  Atmospheric opacity increases Tsys and attenuates signal
  Not as many bright calibrator sources
  Instrument stability is more difficult to maintain
  Antenna accuracy becomes important
  The FOV is smaller
  To overcome some of these difficulties we usually only observe during the winter months (60-65 % chance of suitable 3mm weather) or during the night (especially at 12 or 7mm).
mm observing – the least simple case

## Slide 23
Observe a strong calibrator (e.g. 0537-441, 1253-055 or 1921-295)
  Calibrate delays (dcal)
  Do a pointing (can choose specs)
  Calibrate phase (pcal)
  Calibrate amplitudes (acal or paddle at 3mm)
Observe either 1934-638 (at 12 or 7mm) or a planet (at 3mm) for primary calibration
  Pointing first (1934-638 or source nearby planet)
Target observations
  Include a pointing once an hour (ideally on a strong source within ~20 degrees)
Observing at mm frequencies

## Slide 24
Measure Tsys and correct for the atmosphere at 3mm
  Place an ambient load in front of receiver horn for 30 sec
  Gives Tsys corrected for the current atmospheric conditions
Every ~15 mins (often every second phase cal) and before primary and bandpass calibrators
Paddle scans

## Slide 25
Have a plan and make sure it is a good one!
Different science goals require different strategies so think carefully about what is required
See ATCA webpage for further information and links to other resources:
http://www.narrabri.atnf.csiro.au/observing/
Summary and further information

## Slide 26
Cragg et al. (2005)
Cyganowski et al. (2009)
Turning your plan into a compelling proposal

## Slide 27: A little about the process
  There are two proposal rounds a year (15 Dec and 15 Jun for the APRS and OCTS, respectively)
  The ATNF receives ~150 proposals a semester
  The TAC is made up of 9 members and ~12 readers and they proposals from Parkes, ATCA, Tid and the LBA
  Each proposal is reviewed by two TAC members and two readers
    Each gives a grade and comments
    Grades are finalised during the TAC meeting (held around a month after the proposal deadline)
    Grades given to the scheduler (Jamie for ATCA, Jimi for Parkes)
  On the ATCA ~35% proposals get most of their time, ~15% get some and ~50% get none

## Slide 28: You have your strategy, what next?
For the ATCA, go to opal.atnf.csiro.au and familiarize yourself with the rules, check what arrays are being offered etc
Proposals need
  Coversheet
  Observations table
  Scientific justification

## Slide 29
Know your audience, know the rules
  Write to astronomers but not an expert in your field
  STICK to the rules. 3 pages means 3 pages.
Make it clear what the key question/problem you are
going to address and how you will achieve it
  Don’t wait to explain this!
  What observations are you planning (demonstrate in the technical justification that your plan is good!)? How will they address the problem?
Think about the people reading the proposal
  Make it concise
  Use clear language – please avoid acronyms and jargon
  Make it enjoyable to read – story, background, motivation, what the important question is and how you will answer it. Why is it important? Why are the observations critical to help address the big question?
Use figures
  Make sure that they are relevant and support your proposal
Some advice

## Slide 30: Most annoying things from the last proposal round
Figures – relevance, axis labels!!!!! Please make it so I can read them.
Acronyms!!! Just don’t do it!
Justify the array request, time etc. Just saying you need it isn’t a justification.
Don’t make me hunt for information, either by citing someone without saying what they did, or making me search for stuff on the archive -> saying data x is not good enough is not justification! WHY???
Stick to the page limits and all other instructions.
If resubmitting address the TACs previous comments! If you don’t it will piss the person off from the beginning. Do it! Even if the TAC was wrong!
  SNR, SNRs, SN, CSM, ER, ALMA, ATCA, MWA, GLEAM, ICRAR, CAASTRO, NRAO, ESO, CSIRO, LMC, MCs, CABB, RMS, HI, SINGG, HIPASS, WISE, GALEX, DECam, CTIO, SFE, HST, ISM, SNe, SFR, VLA, HII, ASKAP, GASKAP, RFI, MC, GMC, SMC, UV, CNM, WNM, MW, ANU, CFB, FWHM, LST, WIMP, dSphs, CDM, GBT, EMU, SKA, UFDs, DM, ATOA, CABB, PNe, PN, AGB, IRAS, RMS, BW, IR, AGN, YSO, CMZ, WALLABY, PAF, ASKAPsoft, ACES, SUMSS, ASKAP-12, IMAGINE, BGC, HICAT, JVLA, IRAM, SMA, SDC, NANTEN, SEST, MAGMA, SUPERBx, FRB, SUPERB, GMRT, IGM, GLIMPSE, DM, HESS, LIGO, NSW, TDE, CHIME, MeerKAT, PPTA, CASS, ANDS, CGI, HIPSR, CGM, CSE, LBA, MM1, CM2, HartRAO….....

## Slide 31
  Ask for help and read successful proposals – writing good proposals is a skill that takes time to learn
  Give yourself enough time
  Put your work into broader scientific context and emphasise how the proposed observations address a problem
  Justify technical requirements!
  Make it enjoyable to read
  Use dot points to summaries main points (added benefit that they stand out and draw the reader’s eye)
  Highlight progress in ongoing projects
  Write for a general astronomy audience
Don’t
Do
  Make extra work for the people reading your proposal
  Ignore the TACs comments from previous rounds – explicitly address them
  Add figures unless they are relevant, you explain them and you can READ THE AXIS LABELS
  Use many acronyms
  Wait to deliver the punch line
  Ignore the rules (3 pages means 3 pages!)
  Assume that the TAC readers know why your science is important
  Just say you need a 6D array and a sensitivity of 40 mJy – justify!!!