## Slide 1: Report to ATUC: Engineering Operations & Parkes Development Projects
Erik Lensson, SMIEEE, mSMPTE
Head, Engineering Operations, ATNF
CSIRO Astronomy and Space Science
26 May 2010

## Slide 2: Parkes Remote Operations
HIGH LEVEL OBJECTIVES
Operate & maintain a network of radio telescopes;
Science Operations Centre;
Scheduling improvements;
Reliability;
Rationalise legacy systems;
Health & Safety.
TECHNOLOGIES DEVELOPMENT PROJECTS
‘To enable computer control & monitoring of standard telescope systems’

## Slide 3: Parkes Development Projects
115 - Parkes Drive Control Objective: Computer control of the MCP (manual Control Panel)
117 - Parkes Control & Monitor Objective: Safe, reliable remote monitoring & control of critical telescope systems.
118 - Parkes Receiver Upgrade Objective: Establish a maintainable set of receivers consistent with expected science demand.

## Slide 4: 115 - Parkes Drive Control
OVERVIEW
Replaces the Parkes existing <<< Manual Control Panel (MCP).
New MCP to provide for safe remote operation.
Documented software
Safe remote operation
Working + ‘spare’ MCP

## Slide 5: New Manual Control Panel (MCP)
HIGHLIGHTS
Development platform ‘dummy telescope’ hardware completed >>>
Two MCP’s under construction
Software ‘middleware’ under development to support TCS/EPICS
TIMELINE
Commissioning target: Q1/2011 (expect 3-4 week scheduled 64m telescope shutdown ~ Feb/Mar 2011)

## Slide 6: 117 - Parkes Equipment Control & Monitor
Focus Cabin
  A “remote site”.
  Monitoring & diagnostics for major subsystems (DC power, receivers & translator).
  Video and audio monitoring.
  Vibration monitoring

## Slide 7: Parkes Backend Connections

## Slide 8: RF/IF Switching Matrix
Connecting the Parkes conversion system to the backends
  Replaces manual patch panels with computer controlled switching.
  Consistent configuration scripts for ‘standard’ observations
  Modular commercial off-the-shelf (COTS) hardware (~$196k capital)
  Intelligent (up to 18 GHz) switching under native Linux O/S
  Remote control via Ethernet
  Expandable with additional COTS modules

## Slide 9: Backend Switching

## Slide 10: Parkes Equipment Control & Monitor
Power systems
  Diesel/UPS control
  Remote monitoring, diagnostics
  Synchroniser unit for the generator – reliability and remote control & monitoring.
  TIMELINE
  Backend Switching > Q3/2010
  PECM Overall > Q1/2012

## Slide 11: 118 - Parkes Receiver Rationalisation
Objective: Establish a maintainable set of receivers consistent with expected science demand.
SUB-PROJECT:
L band (H-OH) – Design & fit new improved wideband feed system, to substitute for central beam of Parkes MB receiver;
HIGHLIGHTS/TIMELINE
Order with BAeA;
Delivery imminent;
Marsfield testing;
Install in the next 6 months;
H-OH RX currently @ Marsfield for testing...

## Slide 12: H-OH Receiver (meas.) Performance
Chart: Parkes H/OH Receiver - Performance

## Slide 13: New H-OH (est.) Feed Performance

## Slide 14: 118 - Parkes Receiver Rationalisation
FUTURE PLANS:
S/X band – Modification of MARS receiver package (widen the X-band bandwidth, add S-band LNA’s, design/manufacture new dual-band S/X feedhorn) and add to the Parkes Conversion System ;
C-band – Convert existing K/Ku package with new LNA’s to cover at least 4.8-6.8 GHz (target 4 – 12 GHz);
STATUS: Prototyping and production progress dependent on funding and CSIRO staff Technologies resources.

## Slide 15: Other ‘Horizon 1’ Developments
High Speed VLBI Data Recorder
CISCO Telepresence
CASPSR
CPSR-2
Parkes clock, distribution - Maser (hut, aircon) - Signal distribution, fanout
UPS battery upgrades
  Electrical Power Management Strategy - graceful shutdown - essential vs non-essential

## Slide 16: Thank you 
Contact Us
Phone: 02 6861 1733
Email: erik.lensson@csiro.au Web: www.csiro.au