## Slide 1: The Parkes Single Digital Backend?
Matthew Bailes, Jonathon Kocz, Willem van Straten, Andrew Jameson
Centre for Astrophysics
And
Supercomputing
Swinburne University of Technology
Lister Staveley-Smith
ICRAR/UWA

## Slide 2: Postulate #1:
Given a sufficiently large amount of:
  high-speed A/Ds,
  network bandwidth
  computational power
We can emulate any of the current instruments at Parkes in software.

## Slide 3: ASKAP Single Digital Backend?
192 x 36 x 300 MHz x 2 x 8 bits
  = 33 Tb/s.
13 x 2 x 1 x 400 MHz x 2 x 8
  = 0.166 Tb/s
  Q. Why not start with the Parkes Single Digital Backend with 0.5% of the data and <<1% of the computations?

## Slide 4: Postulate #2:
If we can process the data from the largest bandwidth instruments, we can process the smaller bandwidth instruments.

## Slide 5: Maximum Receiver Bandwidths?
Parkes Multibeam
    13 x 2 x 400 MHz
10-50cm Receiver
    1 GHz at 10cm
    64 MHz at 50cm

## Slide 6: A/Ds?
Require 13 pairs of A/Ds + a couple of spares
Spec:
  8 bits
  2 GHz real samplers (1.6 GHz confirmed in lab)
A/D
A/D
A/D
x13

## Slide 7: Boards
ROACH Boards
3K each + FPGAs (buy 16 for 50K)
4 x 10 Gb ethernet from each
Reprogrammable via Linux
Roach
Roach
Roach
A/D
A/D
A/D
x13

## Slide 8: Data Transport
Commodity off the Shelf 10Gb ethernet
Roach
Roach
Roach
A/D
A/D
A/D
x13
64 Port 10Gb
Ethernet

## Slide 9: VLBI Anyone?
Add 1 Server + a RAID box
Roach
Roach
Roach
A/D
A/D
A/D
x13
64 Port 10Gb
Ethernet
Dell R610
96 TB disk
12.8 Gb/s
10 Gb/s
To Pawsey

## Slide 10: Pulsar Work?
Add Coherent Dedispersion Machines
Roach
Roach
Roach
A/D
A/D
A/D
x13
64 Port 10Gb
Ethernet
96 TB disk
12.8 Gb/s
DeMUX
IB
IB Switch
GPU
GPU
GPU
GPU
GPU
Dell R610
10 Gb/s
To Pawsey

## Slide 11: Pulsar Work?
Add Coherent Dedispersion Machines
Roach
Roach
Roach
A/D
A/D
A/D
x13
64 Port 10Gb
Ethernet
96 TB disk
12.8 Gb/s
DeMUX
IB
IB Switch
GPU
GPU
GPU
GPU
GPU
Dell R610
10 Gb/s
To Pawsey

## Slide 12: Spectroscopy?
Add GPU Machines to make Polyphase Filters
Roach
Roach
Roach
A/D
A/D
A/D
64 Port 10Gb
Ethernet
Dell R610
96 TB disk
12.8 Gb/s
DeMUX
IB
IB Switch
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
x13
x13
X 5
10 Gb/s
To Pawsey
131,072 Channels

## Slide 13: Spectroscopy?
Add GPU Machines to make Polyphase Filters
Roach
Roach
Roach
A/D
A/D
A/D
64 Port 10Gb
Ethernet
Dell R610
96 TB disk
12.8 Gb/s
DeMUX
IB
IB Switch
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
x13
x13
X 5
10 Gb/s
To Pawsey
131,072 Channels

## Slide 14: Pulsar Searching?
Re-use GPU Machines to make 2/4/8-bit Filterbanks
Roach
Roach
Roach
A/D
A/D
A/D
64 Port 10Gb
Ethernet
Dell R610
96 TB disk
12.8 Gb/s
DeMUX
IB
IB Switch
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
x13
x13
X 5
10 Gb/s
To Pawsey
131,072 Channels

## Slide 15: Pulsar Searching?
Re-use GPU Machines to make 2/4/8-bit Filterbanks
Roach
Roach
Roach
A/D
A/D
A/D
64 Port 10Gb
Ethernet
Dell R610
96 TB disk
12.8 Gb/s
DeMUX
IB
IB Switch
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
x13
x13
X 5
10 Gb/s
To Pawsey
131,072 Channels

## Slide 16: Pulsar Searching?
Re-use GPU Machines to make 2/4/8-bit Filterbanks
Roach
Roach
Roach
A/D
A/D
A/D
64 Port 10Gb
Ethernet
Dell R610
96 TB disk
12.8 Gb/s
DeMUX
IB
IB Switch
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
x13
x13
X 5
10 Gb/s
To Pawsey
131,072 Channels

## Slide 17: RFI Mitigation?
Spatial Filtering Techniques:
  Most RFI is in far sidelobes and common to all beams:
13 beams, total power, astonishing correlation.

## Slide 18: RFI Mitigation?
Spatial Filtering Techniques:
  Most RFI is in far sidelobes and common to all beams:
13 beams, total power, astonishing correlation.
Blue = Before RFI mitigation, Red = Afterwards

## Slide 19: RFI Mitigation?
Spatial Filtering Techniques:
  Most RFI is in far sidelobes and common to all beams:
13 beams, total power, astonishing correlation.
Real Pulses!

## Slide 20: RFI Mitigation?
Spatial Filtering Techniques (Kocz & Briggs):
  Group spectra by common frequencies/time
  Determine common signals
  Subtract RFI from voltages?

## Slide 21: RFI Mitigation?
Spatial Filtering Techniques (Kocz & Briggs):
  Group spectra by common frequencies/time
  Determine common signals
  Subtract RFI from voltages?

## Slide 22: Summary
Proposed Backend:
  Is just a big computer.
  Has built-in redundancy.
  Is all software controlled.
  Computers easier to diagnose faults in/replace than Custom FPGA boards.
  Enables new powerful RFI mitigation strategies.